## Slide 1: ECSE 4660/6660: Internetworking of Things
Lecture 3: PHY Layer Fundamentals – Part I
Koushik Kar
ECSE, RPI
Spring 2023

## Slide 2: References
  V. Garg, Wireless Communications & Networking, Morgan Kauffman, 2007. (available as e-book for RPI students)
    Chapter 3: Radio Propagation and Path Loss Models
    Chapter 10: Antennas, Diversity, and Link Analysis
  L. Couch, Digital and Analog Communication Systems, Pearson, 2012.
    Chapter 1: Introduction
    Chapter 8: Wire and Wireless Communication Applications
  C. A. Balanis, Antenna Theory Analysis and Design, Wiley-Interscience, 2005.
    Chapter 1: Antennas
Notes: Part II is next lecture on Digital Modulation

## Slide 3: Recall: Layered Reference Model

## Slide 4: Elements of a Physical (Radio) Link

## Slide 5: Topics to be covered today
Antennas
Signal propagation modes
Thermal Noise

## Slide 6: Introduction
An antenna is an electrical conductor or system of conductors
  Transmission – electrical energy converted to radiated electromagnetic energy into space
  Reception - collects electromagnetic energy from space and converts into electrical
In two-way communication, the same antenna can be used for transmission and reception
  At the same time: Full-duplex
  At different times: Half-duplex

## Slide 7: Sinusoidal Signals and Electromagnetic Waves
How is an Antenna used to communicate?
An electric current element J at some location [1] induces a potential A at other locations, e.g. [2].
If the current J[1] is harmonic in time, the induced potential A[2] is as well.
The induced potential in turn may affect the electric current J[2] at position [2].
By changing a current J[1] we create a delayed and attenuated but still detectable change in current J[2].
Thus, communication can be established by using the effects of electromagnetic disturbance.

## Slide 8: Radiation
Radiation pattern
  An antenna will radiate power in all directions
  Typically, it does not radiate equally in all directions
  The distance from the antenna to each point on the radiation pattern is proportional to the power radiated by the antenna in that direction
An ‘isotropic antenna’
  is an idealized antenna, represented by a point in space that radiates power in all directions equally
  Its radiation pattern is a sphere
Beam width (or half-power beam width)
  Measure of directivity of antenna
Reception pattern
  Receiving antenna’s equivalent to radiation pattern

## Slide 9: Isotropic vs Anisotropic antennas
Isotropic: omni-directional
Anisotropic: directional

## Slide 10: Types of Antennas
Isotropic antenna (idealized)
  Radiates power equally in all directions
Wire antennas
  Dipoles and Vertical Antennas
  Loop antennas
  Helix antennas
[Src: Chapter 1, Balanis]

## Slide 11: Types of Antennas (contd.)
Exact wire shape matters
Simple wire antennas
  Dipole antennas
    Half-wave dipole antenna (or Hertz antenna)
  Vertical antennas
    Quarter-wave vertical antenna (or Marconi antenna)
[Src: Chapter 1, Balanis]

## Slide 12: Types of Antennas (contd.)
Aperture antennas
  Horn antennas
  Conical antennas
  Waveguides
[Src: Chapter 1, Balanis]

## Slide 13: Types of Antennas (contd.)
Microstrip or patch antennas
  Ideal for small devices
    Small footprint
    Printed into ICs
    Easy to make arrays of
[Src: Chapter 1, Balanis]

## Slide 14: Types of Antennas (contd.)
Lens Antennas
  Also called parabolic reflective antenna
[Src: Chapter 1, Balanis]

## Slide 15: Antenna Gain
Antenna gain:
  Power output, in a particular direction, compared to that produced in any direction by a perfect omnidirectional antenna (isotropic antenna)
  The increased power in a given direction is at the expense of other directions
  Refers to directionality, i.e. relative amplification in a certain direction
Effective area
  Related to physical size and shape of antenna

## Slide 16: Antenna Gain (Cont’d)
Relationship between antenna gain and effective area
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light (= 3 x 108 m/s)
    = carrier wavelength
    Note:

## Slide 17: Antenna Gains and Effective Areas
[Src: Chapter 8, Couch]

## Slide 18: Example
Q: A parabolic reflective antenna with a diameter of 2m operating at 12 GHz. Find the antenna gain.
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light (= 3 x 108 m/s)
    = carrier wavelength
Notes: A = pi r^2 = pi
A_e = (from table) 0.56A = 0.56 pi
lambda = c/f = 3 x 10^8 / (12 x 10^9) = 0.025 m.
G = 7A / lambda^2 = 7 pi / (0.025)^2 = 35,186
G_{dB} = 45.46 dB