## Slide 1: ECSE 4660/6660: Internetworking of Things
Lecture 7: Link Layer Fundamentals – Part I
Koushik Kar
ECSE, RPI
Spring 2023

## Slide 2: References
Link Layer Fundamentals: Part I – Random Access MAC Protocols
  Reference for this part:
  A. Kumar, D. Manjunath, J. Kuri, “Communication Networking, An Analytical Approach,” 2004, Elsevier. (Available as E-BOOK through the RPI Library)
  Chapter 8: Sections:
  8.5.2: Carrier Sensing Protocols
  J.F. Kurose, K.W. Ross, “Computer Networking, A Top-Down Approach Featuring the Internet” (7th Ed.).
  Chapter 7: Wireless Networks (to be posted on LMS)
Notes: Part II is next lecture on Digital Modulation

## Slide 3: Recall: Layered Reference Model

## Slide 4: Recall: Physical Layer
Propagation and path loss
  Antennas & propagation
  Compute received signal power
Impairments
  Compute and combat noise and fading
Channel capacity
  Maximum error free transmission rate (Shannon)
Modulation and Coding
  Transmit at different rates depending on SNR of the channel
  Move baseband signal to be centered around carrier frequency (hence we can multiplex)

## Slide 5: Wireless Medium Access Control - Classification
Wireless
MAC
Fixed-Assignment
(for voice oriented networks)
Random Access
(for data-oriented networks)
Hybrid Access Methods

## Slide 6: Wireless MAC Classification
Wireless
MAC
Fixed-Assignment
(for voice oriented networks)
Random Access
(for data-oriented networks)
Hybrid Access Methods

## Slide 7: “Fixed”-Assignment MAC
All existing voice-oriented wireless networks, such as cellular telephony or PCS services, use fixed-assignment channel partitioning techniques
A fixed allocation of channels are made on a predetermined basis to a single user for the duration of the communication session.
Channels are formed by allocating different frequencies (FDMA), time slots (TDMA), or spread spectrum codes (CDMA).
Choice has a great impact on the network performance, to the extent that various voice-oriented wireless systems are commonly referred to by their channel access method (although it is only a part of the layer two specification!).
Notes: “Fixed” for a certain duration of the specific session/voice-call/circuit

## Slide 8: Wireless MAC: A Simple Classification
Wireless
MAC
Fixed-Assignment
(for voice oriented networks)
Random Access
(for data-oriented networks)
Hybrid Access Methods

## Slide 9: Random Access MAC Classification
Two broad classes of random access methods:
  ALOHA-based random access methods [Abramson70]
    Used mainly for wide-area data networks
  Carrier-sense based random access methods
    Used mainly for wireless LANs
    Hidden terminal and exposed terminal problems
    From CSMA/CD to CSMA/CA
    CSMA/CA with RTS/CTS (MACA, MACAW, etc.)
    Priority and Fairness
    Power conservation
    MAC for directional antennas

## Slide 10: Random Access MAC
Evolved around bursty data applications in computer networks.
Fixed-assignment methods
  make relatively efficient use of communications resources only when each user has a steady flow of information to be transmitted during each session
  Could be a waste of resources for intermittent traffic
  Require an “arbitrator”
Random access methods provide more flexible and efficient ways of managing medium access for short bursty messages
  Could think of them as distributed statistical multiplexing techniques
A natural consequence is that there is contention among the users for access to the medium channels – manifested in “collisions” of contending transmissions
These methods are sometimes called contention schemes
Mainly used in wired and wireless LANs and data-oriented WANs

## Slide 11: CSMA: Carrier Sense Multiple Access
CS: Sense the channel
  If idle, transmit
  If busy, wait and sense again in the future
Collisions might happen
  If more than one user senses the channel “at the same time”
  Collision window
  Need a solution for this problem!

## Slide 12: CSMA/CD
CD: collision detection
  While transmitting, simultaneously listen to the channel for collisions (i.e. other transmissions) – this is rather easy in wired systems, and difficult in wireless systems.
  Collision detection: power higher than expected for a single communication
  If detected, stop transmission, send a jam signal, and reschedule for another time

## Slide 13: Difference Between Wired and Wireless Random Access MAC
If both A and C sense the channel to be idle at the same time, they send at the same time.
Collision can be detected at sender in Wired LANs (Ethernet) using CSMA/CD
In wireless, it might not be possible to detect collision at sender, so CSMA/CD doesn’t work
A
B
C
A
B
C
Ethernet LAN
Wireless LAN

## Slide 14: From CSMA/CD to CSMA/CA
Thus CSMA/CD is used in IEEE 802.3 (i.e. wired Ethernet) but not in IEEE 802.11 (i.e. WiFi)
So we use CSMA/CA for wireless
  CA here refers to the fact that we can not detect collisions
  So how do we detect collision?

## Slide 15: MAC: from wired to wireless
Can we apply the same MAC methods of wired networks to wireless networks?
CSMA/CD
  “Sense” the medium, send as soon as the medium is free, and listen to the medium to “detect collisions”
CSMA/CD does not work in wireless networks
  Signal strength decreases proportional to the square of the distance (assuming free space propagation)  Hidden Terminal and Exposed Terminal problems
    Sender would apply CS and CD, but collisions happen at the receiver
    Might be the case that a sender cannot “hear” the collision or cannot “sense” another carrier at the receiver

## Slide 16: Exposed Terminal Problem
Exposed terminals (A valid comm can not take place because the sender is exposed)
  A starts sending to B.
  C senses carrier, finds medium in use and has to wait for A->B to end.
  D is outside the range of A, therefore waiting is not necessary.
  A and C are “exposed” terminals i.e. A and C could communicate to their receivers at the same time (since their receivers are far apart), but because A and C are exposed to each other (i.e. can hear each other), one of them needlessly refrains from transmitting.
A->B and C->D transmissions could have taken place in parallel without collisions, but CS function will only allow one of them
A
B
C
D

## Slide 17: Hidden Terminal Problem [Tobagi75]
Hidden terminals: A node within the range of two nodes that are out of range
  A and C cannot hear each other.
  A sends to B, C cannot receive A.
  C wants to send to B, C senses a “free” medium (CS fails)
  Collision occurs at B.
  A cannot hear the collision (CD fails).
  A is “hidden” from C with respect to transmissions to B.
Solution?
  Hidden terminal is peculiar to wireless (not found in wired)
  Need to sense carrier at receiver, not sender!
  “virtual carrier sensing”: Sender (node C) “asks” receiver (node B) whether it senses the channel is busy. If so, behave as if channel busy.
B
A
C

## Slide 18: RTS/CTS solution of Hidden Terminal Problem
A
B
C
RTS
CTS
Data
ACK
C knows B is listening
to A. Will not attempt to
transmit to B.
Hidden Terminal Problem Solved
through RTS-CTS exchange!
CTS

## Slide 19: CSMA/CA + RTS/CTS (Contd.)
802.11 DCF MAC:
  CSMA/CA
  Control packet transmissions precede data packet transmissions to facilitate collision avoidance
  4-way (RTS, CTS, Data, ACK) exchange for every data packet transmission
Can there be collisions? Yes.
  Control packet collisions (C transmitting RTS at the same time as A)
  C does not register B’s CTS
  C moves into B’s range after B’s CTS

## Slide 20: CSMA/CA+RTS/CTS Algorithm
Sense channel (CS)
If busy
  Freeze backoff timer
Else
  Send RTS
  If CTS not received
    Back-off to try again later
  Else
    Send Data
    If ACK not received
      Back-off to try again later
    Next packet processing

## Slide 21: CSMA/CA Algorithm (Contd.)
Maintain a value CW (ContentionWindow)
If Busy,
  Wait till channel is idle. Then choose a random number between 0 and CW and start a back-off timer for proportional amount of time.
  If transmissions within back-off amount of time, freeze back-off timer and start it once channel becomes idle again.
If Collisions (Control or Data)
  Binary exponential increase (doubling) of CW

## Slide 22: DCF Example
data
wait
B1
B2
B1
B2
data
wait
B1 and B2 are backoff intervals
at nodes 1 and 2
B2

## Slide 23: Backoff Interval
The time spent counting down backoff intervals is a part of MAC overhead
Choosing a large cw leads to large backoff intervals and can result in larger overhead
Choosing a small cw leads to a larger number of collisions (when two nodes count down to 0 simultaneously)

## Slide 24
Since the number of nodes attempting to transmit simultaneously may change with time, some mechanism to manage contention is needed
IEEE 802.11 DCF: contention window cw is chosen dynamically depending on collision occurrence

## Slide 25: Binary Exponential Backoff in DCF
When a node fails to receive CTS in response to its RTS, it increases the contention window
  cw is doubled (up to an upper bound)
When a node successfully completes a data transfer, it restores cw to Cwmin
cw follows a sawtooth curve

## Slide 26: IEEE 802.11 (next lecture)
The 802.11 standard
  MAC and PHY functionality for wireless connectivity of fixed, portable and moving stations moving at pedestrian and vehicular speeds within a local area.
Specific features of the 802.11 standard include the following:
  Operates at either 2.4 GHz or 5 GHz unlicensed ISM bands
  Supports transmission rates of 1, 2, 11, and 54 Mbps.
  MIMO: n: 150Mbps, ac: 780Mbps
  Support Multicast/broadcast services
  Network management services
  Registration and authentication services
  In certain modes, could support asynchronous and time-bounded delivery service